TOWN OF GREENWOOD

PERMIT & INSPECTION PROCEDURES

- Applicant must fill out the application completely.

- All fees must be paid to the Town of Greenwood and Steve Grayson before the permit can be issued.

- The application is not the permit.

- State license number must be checked with Louisiana State Licensing Board

- Residential new, addition & remodel permits cannot be issued until the plan review is complete.

- Commercial new, addition & remodel permits cannot be issued until the plan review is complete and a fire marshal letter has been provided.

- A copy of all permits must be provided to Steve Grayson.  Receipt attached to the permit.

- All inspection request and any other questions must be called in to Steve Grayson (318-426-4992).  Special time and appointments can be requested to make the inspection.  All inspections will be made within 48 hours of the inspection request.

- On new, additions and remodel permits; electrical, plumbing, mechanical & building inspections will be made at the same time.

- The following inspections are required:

ELECTRICAL

Saw Service

1st – under slab (concrete encased electrode and under slab conduit)

2nd – Wall rough

3rd – final

Temporary Power (trench depth if applicable)

MECHANICAL

1st – rough (supply, return, exhaust & outside air duct), condensate pipe

2nd – final (unit placement, duct pressure test, final connections)

PLUMBING

1ST – under slab with pressure test on drain & water pipe

2nd – wall rough (pressure test on water pipes and gas pipes), main vent thru roof

3rd – final (fixture connection of all drain, vent, water and gas piping)

BUILDING

1st – foundation (footing depth and width, slab thickness & elevation, vapor barrier, re-bar placement)

2nd – wall rough (stud spacing, king & jack studs, headers, ceiling joists, roof rafters and supports, roof decking, wall insulation, bracing & vapor barrier)

3rd - final