## Slide 1: CANBY CREEK WATERSHED PROJECT R-1
COMMONLY KNOWN AS
DEL CLARK LAKE/STONEHILL PARK

## Slide 2: PROJECT PURPOSE
WATERSHED PROTECTION
FLOOD PREVENTION
RECREATION

## Slide 3: LOCATION
Canby Creek Watershed is located in west central Minnesota, in the Minnesota River Subbasin portion of the Mississippi River Basin.
Structure R-1 is located in Norman Township, Sections 8 & 9, Yellow Medicine County.
Structure R-4 is located in Norman Township, Section 5, Yellow Medicine County.
Structure R-6 is located in Fortier Township, Section 14, Yellow Medicine County.

## Slide 4
Canby Creek Watershed is approximately 2.5 miles wide and 12 miles long.
The maximum elevation in the watershed is 1,785 feet and the minimum is 1, 188 feet above mean sea level.
The grade of Canby Creek varies from 15 to 68 feet per mile.

## Slide 5
A severe rainstorm occurred in the watershed on July 26, 1963. Although no attempt was made to determine the aerial extent of the storm, 5.2 inches of rain fell in three hours in Canby. According to the “Canby News”, two people were injured (one hospitalized) and several families had to be evacuated from their homes with boats. Highway No. 68 was closed within the city limits where water inundated the highway. Highway No. 75 was inundated for three-fourths of a mile northeast of Canby.

## Slide 6
A survey was taken by the City of Canby to determine the monetary losses caused by this flood. Following is a summary of the results of the survey for the Canby area:
City of Canby Municipal property $16,650.00
City of Canby Personal Property $18,369.10
City of Canby Business Property $12,013.70
Railroad Property $20,000.00
Farm Property $ 5,550.00
State Property $ 1,700.00
County Property $ 7,620.00
TOTAL $81,902.80

## Slide 7
Local Residents felt that loss of life and much more serious damages were prevented because numerous volunteers assisted in evacuating people and moving property to higher elevations.

## Slide 8
Floodwater damages occured in the City of Canby on the average of once every five years from excess rainfall runoff and once every seven years from snowmelt runoff. Although floods from snowmelt runoff are not as frequent as floods from excess rainfall, the snowmelt runoff usually causes more damage.

## Slide 9
The 1974 Final Environmental Impact Statement noted that the basements, first floors, and lawns of 22 homes and three business places along Canby Creek were subject to damage from floodwaters. Property values of these places, as well as an additional 35 homes located adjacent to the flood plain were reduced. The basements and lawns of 58 homes and 2 business places located in the northwestern part of Canby were subject to flood damage from the overflow of County ditch #19. Property values of these places, as well as an additional 25 homes located adjacent to the flood-prone areas, have been reduced.

## Slide 10
Floodwater damage also occurs to roads, bridges, fences, & crops and pasture located downstream from Canby Creek Watershed to the junction of the Lac qui Parle River. Approximately 50 farm families were affected by the flooding conditions of which 10 were located within the watershed and the remaining 40 located downstream.

## Slide 11
In 1963 the Canby Watershed Steering Committee was formed and met with the SWCD to start planning for the Canby Creek Project.
In 1972 the project was turned over to the Lac qui Parle-Yellow Bank Watershed District to be the sponsoring agency for the project.

## Slide 12
The Yellow Medicine & Lincoln County SWCD’s worked with landowners to develop soil & water conservation plans on farmland upstream of the project. 53% of the land upstream of the structural measures were treated with the application of conservation practices such as grassed waterways, grade stabilization structures, crop residue management, contour farming, stripcropping, terraces, field windbreaks, pasture & hayland management to name a few.

## Slide 13
The Canby Creek Watershed Project consists of Structures R-1, R-6, & R-4 which control a drainage area of 28.19 square miles of the 30.2 square miles above State Highway No. 68.

## Slide 14
Structure R-4 provides flood protection for the northwest part of Canby. The structure controls runoff from a 2.36 square mile drainage area. This structure was built in 1982.

## Slide 15
Structure R-6 wsa planned upstream from R-1 and will assist R-1 in providing flood protection to Canby and agricultural areas downstream The structure controls the runoff on 15.46 square miles of drainage area. This structure was built in 1981.

## Slide 16
Structure R-1 (more commonly known as Del Clark Lake). This structure is located downstream from R-6 and controls an additonal 10.37 square mile of drainage area.
The recreational area (campground) was planned on 275 acres of land adjacent to the 147-acre lake created by structure R-1.

## Slide 17
Two grade stabilization structures and 0.8 mile of stream channel stabilization were installed in Canby Creek from State Highway #68 downstream to the first north-south township road.

## Slide 18
On May 31, 1986 a dedication ceremony was held on the Canby Creek Dam Project.
The R-1 structure was awarded a “7 wonders of Engineering” award in 1986.

## Slide 19
Federal Cost-share from Watershed Protection & Flood Prevention Act, Public Law 566, 83rd Congress.
Lac qui Parle-Yellow Bank Watershed District other costs & through assessments.
County & Townships for culvert & bridge maintenance responsibility of County & Townships.