610 OPERATION

DO NOT PUSH RESET SWITCH UNTIL FIRE DEPARTMENT AUTHORIZES RESET

FOR A “TROUBLE DISPLAY “CALL 458-3249.

FOR A “SUPV DISPLAY” CALL 458-3249

FOR  “ALARM DISPLAY “ GO TO DEVICE IN ALARM THAT 	IS LISTED ON SCREEN AS BEING IN ALARM - IF PULL STATION, PULL HANDLE WILL BE PULLED DOWN - IF SMOKE OR HEAT DETECTOR THE L.E.D. WILL BE ON(solid red light).  NORMAL FOR ALL DEVICES IS BLINKING L.E.D. 	OR NO BLINKING ON DEVICE.

ONCE DEVICE IN ALARM IS LOCATED, VERIFY NO FIRE CONDITION EXISTS. IF FIRE EMERGENCY EXISTS CALL 	911 TO REPORT.  IF NO FIRE CONDITION EXISTS PUSH THE “SIGNAL SILENCE” SWITCH.  STROBES WILL REMAIN ON UNTIL RESET.

RESET PULL STATION HANDLE BY OPENING PULL STATION WITH KEY THAT IS ATTACHED TO THIS NOTICE (if  pull station is not key type loosen screw on top of pull station with small screw driver to open) AND SET SWITCH INSIDE PULL STATION TO NORMAL, THEN CLOSE PULL STATION.

IF SMOKE OR HEAT DETECTOR WAS SET OFF BY KNOWN 	SOURCE CORRECT CAUSE BEFORE RESETTING PANEL.  IF 	UNKNOWN SOURCE CALL TECHNICIAN ON DUTY (458-3429)

AFTER FIRE DEPARTMENT HAS AUTHORIZED RESET AND 	DEVICE IN ALARM IS CLEARED OF CAUSE OF ALARM 	THEN PUSH “RESET” SWITCH

“DAY” SWITCH” NOT USED.

“DRILL” SWITCH” DO NOT PUSH.

ANY QUESTIONS CALL 458-3249 FOR TECHNICIAN ON DUTY