AccuTel-Edens Telecom, Inc.

(910) 395-6166

www.accutelnc.com

PROGRAMMING SYSTEM SPEED DIALS:  (ESI SYSTEMS)

FROM ANY MULTILINE PHONE:

1) PRESS PROGRAM or PROG/HELP, HOLD, DIAL 456, PRESS #

2) LISTEN TO MENU, PRESS 1, 7

3) ENTER THE SPEED DIAL CODE NUMBER (600-699),  THEN PRESS #

4) SPELL NAME BY USING DIAL PAD KEYS (press # to enter each letter)

PRESS # TO SAVE COMPLETE NAME WHEN FINISHED

( EX.  IF NAME BEGINS WITH “S”  THE NAME KEY WILL BE THE 7

BUTTON ON THE DIAL PAD BECAUSE THIS IS WHERE “S” IS LOCATED AND YOU WILL

PRESS THE 7 KEY THREE TIMES TO SELECT  “S” AS THE CHARACTER )

NOTE: USE O BUTTON FOR HYPHENS OR DASHES

USE 1 BUTTON FOR SPACES

5) ENTER LINE ACCESS CODE (usually 9) PLUS THE PHONE NUMBER TO STORE, PRESS #

ex.  To store 1-704-555-1212  enter:  917045551212

6) REPEAT STEPS 3, 4, 5 ABOVE FOR OTHER SYSTEM SPEED DIALS

7) WHEN FINISHED, PRESS # TO GET BACK TO MAIN MENU AND HANG UP

(main menu= “For System Function Programming…” )

----------------------------------------------------------------------------------------------------------------------

HOW TO CHANGE THE TIME AND DATE OF THE SYSTEM:

FROM ANY MULTILINE PHONE:

1) PRESS PROGRAM or PROG/HELP, HOLD, DIAL 456, PRESS #

2) PRESS 1, 4

3) PRESS 1 TO SET TIME AND DATE

4) FOLLOW INSTRUCTIONS FROM THIS POINT

NOTE: YOU WILL FIRST ENTER TIME IN TWELVE HOUR FORMAT: 1233= 12:33 OR 330=3:30

SELECT  AM OR PM BY USING THE SCROLL KEYS BESIDE THE ESI DEX BUTTON

ENTER DATE: MMDDYYYY   EX: 07052002 = JULY 7, 2002

PRESS # TO SAVE ALL YOUR ENTRIES