## Slide 1
Analytical Methods Used to Detect PFOA and Related Substances in Various Matrices: Is there a standard analytical method?
Angela M. Lynch1, Anthony Bonnet3, Andrew Kahn3, Shin-ya Seiji4, Stephen Korzeniowski5, Takayuki Nakamura6, Marco Malvasi7, Carole Mislin2, Marissa Maier8, Ranjit Machado8
1FluoroCouncil, 2Archroma Management, LLC , 3Arkema France,4Asahi Glass Co, Ltd, 5The Chemours Company, LLC,6 Daikin Industries, Ltd., 7Solvay Specialty Polymers, 8Environ International Ltd.
ABSTRACT
RESULTS
ECHA has proposed a restriction on the manufacture, use, and sale of mixtures and articles containing PFOA or PFOA-related substances at concentrations exceeding 2 ppb. In order to set such restrictive concentrations of chemicals, analytical methods must have the sensitivity, reliability, and accuracy to consistently measure at those concentrations. In response to the proposal, we conducted a review of the analytical methods that are available to measure PFOA and PFOA-related substances in fluoropolymer and fluorotelomer products and determine whether these substances can be reliably quantified at the proposed 2 ppb threshold. To conduct this review, peer-reviewed publically available studies and member company information were gathered and reviewed.
CONCLUSIONS
The European Chemical Agency (ECHA) recently proposed to restrict the use, manufacture and sale of mixtures and articles containing PFOA and PFOA-related substances at concentrations exceeding 2 ppb (ECHA, 2014). We questioned whether a standard analytical method exists to evaluate such levels in fluoropolymer and fluorotelomer products. To answer the question, analytical methods used to evaluate these substances in various matrices were reviewed from the published literature as well as collected from FluoroCouncil member companies. The results indicate that high performance liquid chromatography coupled to tandem mass spectrometry (LC/MS/MS) is consistently used for PFOA analysis, however, for 8:2 fluorotelomer alcohol (FTOH) and 8:2 monomers, methods vary. Also, results indicate that analytical sensitivity is highly dependent on the extraction of the substance from the matrix and the control of analytical interference. PFOA in textiles is the only category of fluorotelomer products identified with a limit of quantification (LOQ) less than 5 ppb (Larson, 2006; Mawn, 2006; Stadalius, 2006; Liu, 2009; Guo, 2009; Shao, 2012). PFOA-related substances have also been analyzed in consumer products (Knepper et al., 2014; Liu et al., 2014). Therefore, it is not feasible to apply a 2 ppb threshold concentration of PFOA and PFOA-related substances to all fluoropolymer and fluorotelomer products.
Based on this review, high performance liquid chromatography with tandem mass spectrometry (LC/MS/MS) is the preferred method for PFOA analysis in fluoropolymer and fluorotelomer products (Table 1). Depending upon the product, PFOA may be extracted from the sample medium using a solvent, such as methanol, and an isotopically labeled standard may also be used to reduce matrix effects. There is less consistency, however, in the analytical methods used to measure 8:2 FTOH and 8:2 monomer in fluorotelomer products; gas chromatography with mass spectrometry (GC/MS), gas chromatography with tandem mass spectrometry (GC/MS/MS), and LC/MS/MS are all commonly used.
With respect to analytical sensitivity, low quantification limits may be achieved if the target compound can be readily extracted from the sample matrix and analytical interferences are minimal. For example, a limit of quantification (LOQ) in the low ppb range (less than 5 ppb) appears to be achievable for PFOA in textiles (Mawn et al. 2005, Stadalius et al. 2006, Liu et al. 2009, Guo et al. 2009, Shao 2012). Other products, however, may be more complex and LOQs for PFOA may be substantially higher. For example, a relatively wide range of LOQs have been reported for PFOA in fluoropolymers and fluorotelomer products sold for textile applications (Table 1). This could be due to variability in the composition of these products, matrix effects, analytical interferences, or background contamination. Accordingly, PFOA in textiles is the only category of fluorotelomer products that could accurately be quanitified at the 2 ppb PFOA threshold proposed by ECHA.
In conclusion, while it is possible to identify products where a 2 ppb threshold could apply, a single threshold cannot be applied to all fluoropolymer and fluorotelomer products. These products may have a range of detection and quantification limits, which could span several orders of magnitude. As a result, thresholds must be developed on a product by product and constituent by constituent basis. For these reasons, it is inappropriate to universally apply a 2 ppb threshold based on an LOQ for PFOA in textiles, as ECHA is attempting to do using the results of the Mawn et al. 2005 study.
REFERENCES
Guo, Z. et al. 2009. Perfluorocarboxylic Acid Content in 116 Articles of Commerce. EPA/600/R-09/033. March.
Larsen et al. 2006. Method development for the determination of residual fluorotelomer raw materials and perfluorooctanoate in fluorotelomer- based products by gas chromatography and liquid chromatography mass spectrometry. Journal of Chromatography A. 1110(1-2): 117-124.
Liu et al. 2009. Method development for liquid chromatographic/triple quadrupole mass spectrometric analysis of trace level perfluorocarboxylic acids in articles of commerce. Journal of Chromatography A. 1216:3910-3918.
Mawn et al. 2005. Determination of extractable perfluorooctanoic acid (PFOA) in water, sweat simulant, saliva simulant, and methanol from textile and carpet samples by LC /MS /MS. Analyst. 130(5):670-678.
PERFORCE. 2006. Perfluorinated Organic Compounds in the European Environment.
Risha et al. 2005. Method for Trace Level Analysis of C8, C9, C10, C11, and C13 Perfluorocarbon Carboxylic Acids in Water. Anal. Chem. 77:1503-1508.
Shao, C., Wang, L. 2012. Determination of perfluorooctanoic acid (PFOA) and perfluorooctanesulfonic acid (PFOSA) at ng g-1 levels in textiles by GC-μECD. 244th ACS National Meeting & Exposition, Philadelphia, PA, United States, August 19-23, 2012.
Stadalius, M. et al. 2006. A method for the low-level (ng g(-1)) determination of perfluorooctanoate in paper and textile by liquid chromatography with tandem mass spectrometry. J. Chromatography Science. 1123(1): 10-14
INTRODUCTION/METHODS
A substantially higher range of LOQs have also been reported for 8:2 FTOH and 8:2 monomer in fluorotelomer products (Table 2).