## 进入夏季篇---房屋维护Home Maintenance Tips（转载）

2015-04-27 HunterYu

1.Clean lint from clothes dryer vent, from the dryer drum to where the air is vented outdoors. 清理烘干机通风管道（去除衣物纤维灰尘等形成的絮状物）

2.Repair or replace damaged window screens and weather-stripping. Caulk open joints, particularly around windows and doors. 修理或更换纱窗和密封条。检查门窗周围的密封胶。

3.Repair or replace gates, fence posts, landscape borders, etc.修理或更换3院门，院墙篱笆等。

4.Clean decks, gazebos, fences and patio furniture. Refinish if needed. 清理室外平台，露台及室外家具。必要时重新刷漆。

5.Carefully climb on the roof (provided the roofing materials can be walked on)and inspect it or have a qualified roofer do it for you. Look for damage to shakes, shingles or tiles. Inspect anything that protrudes through the roof for rust, open seams or other damage. Be careful. 如果能上屋顶或请人，检查屋顶瓦片有无破损。检查任何屋顶突出物，看有无锈蚀，开缝或其他损坏。

6.Check exterior walls for cracks, peeling paint or other damage. 检查外墙。看有无开裂，油漆脱落或其他问题。

7.Trim branches around the roof line to keep squirrels and other pesky animals off the roof. 剪除靠屋顶太近的树枝。

8.Clean underside of range hood and clean or replace filters. 清理抽油烟机里侧或更换滤网。

9.Clean condenser coils or fins beneath or behind refrigerator, according to the manufacturer's instructions. Check to be certain there is adequate air flow around the appliance. 按照厂家使用说明清理冰箱背后（或下面）的冷凝线圈/板。检查冰箱四周是否留了足够的空间。

10.Inspect water heater for leaks and flush tank. Test temperature and pressure relief (TPR) valve according to the manufacturer's instructions. 检查热水器是否泄漏并冲洗水箱(打开排水阀门放水3 分钟以延长寿命，不用动任何其他开关或阀门)。根据使用手册检查TPR 开关。

11.Paint the inside of your house if needed. 室内重新油漆的好季节。

12.Check for leaks at valve where water enters the house, at outdoor faucets and any valves to fixtures, such as to toilet, bathroom or kitchen sink, bar, etc. Turn each off and on several times to make certain they operate properly. Check for leaks.检查各处给水开关，入户，室外，到卫生间，厨房等。各处开关打开关闭几次查有无泄漏。

13.Inspect grout around sinks, tubs and showers. Repair or replace damaged areas.检查水槽，浴盆，淋浴等处的勾缝和密封。及时修理更换破损处。

(文章来源于网络，向原作者表示敬意。如有版权问题，联系我们，我们将第一时间删除.)