Location

Lisbon, Ohio

Facility Type

Construction and Demolition Debris   Landfill, Solid Waste

Client

R. B. Jergens, Contractors, Inc.

Services Provided

- Construction Inspection/Quality Assurance and Construction Certification Reporting

- Landfill Design

- Soils Pre-qualification

- Construction Administration

Aerial View of Construction

Installation of Explosive Gas Vent and Monitor

Project Description

As a subcontractor to R. B. Jergens, NPE provided engineering design, permitting, soils pre-qualification, oversight of a geoprobe boring program, and construction quality assurance/ certification services for the construction of a 46-acre final cap system.

This project represented the first time that the Ohio EPA ever managed a landfill closure project.  Elements of the work included the construction of a cap system subbase layer, odor control system, 40-mil LLDPE geomembrane, geocomposite drainage layer, protective cover soil, perimeter drainage swales, and passive gas vents.  NPE assisted the earthwork contractor with project administration.

Installation of Cap Geomembrane

Installation of Rock Channel Protection