ORD. AMDT    , 11-12

AMENDING CHAPTER 10 OF THE DANE COUNTY CODE OF ORDINANCES, REGARDING MINERAL EXTRACTION CONDITIONAL USE PERMIT APPLICATION REQUIREMENTS

The County Board of Supervisors of the County of Dane does ordain as follows:

ARTICLE 1.  Unless otherwise expressly stated herein, all references to section and chapter numbers are to those of the Dane County Code of Ordinances.

ARTICLE 2.  Section 10.191(2) is amended to read as follows:

(2)	The application for the conditional use permit necessary to conduct a mineral extraction operation shall include the following information:

- A legal description of the land for which the permit is requested.

  - This may be a Lot in a Certified Survey Map, a Lot (and Block, if any) in a Subdivision, or an exact “metes and bounds” legal description prepared by a qualified professional.

  - The description must include the size of the CUP area in acres or square feet.

- Tax parcel number(s) of the lot(s) or parcel(s) where the conditional use is to be located.  If the area proposed for the conditional use is a part of a larger parcel, applicant must provide the tax parcel number of the larger parcel.

- A written statement containing the following information:

  - General description of the operation.

  - Existing use of the land.

  - Existing natural features including approximate depth to groundwater.

  - The types and quantities of materials that would be extracted.

  - Proposed dates to begin extraction, end extraction, and complete reclamation.

  - Proposed hours and days of operation.

  - Geologic composition and depth to the mineral deposit.

  - Identify all major proposed haul routes to the nearest Class A highway or truck route.  Indicate traffic flow patterns.

  - Proposed phasing plan, if any (recommended for larger sites).

  - Types, quantities, and frequency of use of equipment to extract, process, and haul.

  - Whether and how frequently blasting, drilling, mining, crushing, screening, washing, refueling, fuel storage, asphalt batching, or concrete mixing would be performed on site.

  - Whether excavation will occur below the water table and, if so, how ground water quality will be protected.

  - Any proposed temporary or permanent structures (e.g., scales, offices).

  - Any special measures that will be used for spill prevention and control, dust control, transportation, or environmental protection.

  - Proposed use after reclamation as consistent with Chapter 74.

- In addition to the submittal requirements enumerated in sec. 10.255(e), applications for a mineral extraction conditional use permit shall include a Site/Operations Plan prepared by a qualified professional, drawn to a measurable scale large enough to show detail and at least 11” by 17” in size, showing the following information:

  - Boundaries of the permit area and of the extraction site.

  - Zoning district boundaries in the immediate area. Label all zoning districts on the subject property and on all neighboring properties.

  - Existing contour lines (not more than 10 foot intervals).

  - Existing natural features including lakes, perennial / navigable streams, intermittent streams, floodplains, wetlands, drainage patterns, and archaeological features.

  - Existing roads, driveways, and utilities. Show width of all driveway entrances onto public and private roadways.

  - All residences within 1,000 feet of the property.

  - Specific location of proposed extraction area, staging area, equipment storage.

  - Proposed location and surfacing of driveways.

  - Proposed phasing plan, if any (recommended for larger sites).

  - Proposed fencing of property, if any, and gating of driveways.

  - Proposed location of stockpiles.

  - Proposed location and type of screening berms and landscaping.

  - Proposed temporary and permanent structures, including scales and offices.

  - Proposed signage, if any.

- An erosion control plan, drawn to scale by a professional engineer, meeting all applicable state and county requirements.

- A reclamation plan prepared in accordance with the Wisconsin Administrative Code and the Dane County Non-metallic Mining Reclamation Ordinance.

[EXPLANATION: This amendment is proposed to provide a uniform and consistent set of submittal requirements for mineral extraction conditional use permit applications.  The amendment is complimentary to existing conditional use permit application requirements from sec. 10.255(2)(e), and addresses issues specific to mineral extraction operations.  The amendment reflects current administrative requirements.]