C3 Body Lift Punch List

1. Battery
  1. Battery Negative terminal – Disconnect from frame
  2. Battery Postive terminal – Disconnect from starter and remove from clip
  3. Battery Positive Cable bracket (if applicable) – Disconnect from bell housing
2. Steering Column
  1. Disconnect and remove rag joint
    1. This usually requires either dropping the steering box or the steering column
3. Brakes
  1. Disconnect Master Cylinder lines to proportioning valve
  2. Disconnect vacuum line to power booster
  3. Disconnect proportioning valve wire
4. Manual transmission
  1. Disconnect clutch pedal rod clip only
  2. Disconnect back-up light plug
  3. Disconnect speedometer cable
  4. Remove chrome ball from shifter
  5. Remove shifter cover plate
  6. Remove shifter dust cover from transmission housing tunnel
5. Automatic transmission
  1. Disconnect speedometer cable
  2. Disconnect any electrical plugs
6. Accelerator Pedal
  1. Disconnect throttle cable from carburetor
7. Engine
  1. Disconnect all engine wiring as applicable (temperature sending unit(s), oil pressure sending unit, tachometer wire, distributor coil plug, electronic choke plug, injector plug, compressor plugs, alternator plug, a/c pressure sensor, etc.)
  2. Disconnect all vacuum lines as applicable (manifold to firewall, manifold to lights, manifold to cruise control, evaporator cannister, etc.)
8. Air conditioning
Disconnect compressor lines to evaporator
1. Heater
  1. Disconnect hot water line from vacuum cut off and remove from any clamps or hoops
  2. Disconnect return line from heater core
2. Coolant Reservoir
  1. Disconnect hose from radiator
3. Radiator
  1. Remove hood and hinges
  2. Remove bolts from sides of radiator support bracket
4. Headlights
  1. Remove vacuum lines from ballast tank (if tank is bolted to frame)
5. Front end
  1. Remove urethane bumper cover
  2. Remove front air dam
  3. Remove valence panel
  4. Remove bumper support bolts (frame extensions, center supports, lower support, etc) and bumper
  5. Remove frame extensions
6. Parking Brake
  1. Remove pulley from cross member
  2. Remove main cable from cross cable
7. Rear end
  1. Unplug license plate light and spare tire light
  2. Unplug rear lights
  3. Remove rear tail and backup lights
  4. Remove urethane bumper cover
  5. Remove bumper mount bolts and bumper
8. Antenna
  1. Disconnect antenna grounding strap from frame
9. Gas Tank
  1. Remove wire from gas tank sending unit
10. #1 left and right body mount
  1. Remove splash shield
  2. Remove #1 body mount bolt (probably requires cutting)
11. #2 left and right body mount
  1. Remove kick panel
  2. Remove #2 bolt
12. #3 left and right body mount
  1. Remove access plate in rear fender
  2. Remove #3 bolt
13. #4 left and right body bolt
  1. Remove rear speaker cover and speaker
  2. Access hole in rear and remove #4 bolt