## Slide 1: PAULOWNIA PRIMED WOOD TRIM & PATTERN
SANTIAM LUMBER SALES

## Slide 2: PLANTATION GROWN

## Slide 3: Paulownia-A Soft Hardwood
General Characteristics | Product Offered
Wood Structure | Boards & Dimension
Wood Properties | Pattern Stock
Wood Utilization/Uses | Bevel Sidings
Summary of Benefit | Plant Processing
Paulownia - A Soft Hardwood

## Slide 4: General Characteristic
Paulownia is a soft hardwood native to China. The heartwood is light in color and the sapwood even lighter. Color differential between the two is not distinct. The wood is without odor or taste and is mostly free from knots. Planed or sanded, it has the feel of spun silk.
Wood Structure
The demarcation between heartwood and sapwood is not clear and the wood is straight grained and lustrous.
Wood Properties
Paulownia is comparatively soft and light in weight for a hardwood. Physical weight is slightly less than kiln dried western red cedar. It is low in overall strength, but has a high strength to weight ratio. The shrinkage coefficient is smaller than most commercially harvested coniferous and broad leaf woods. The wood dries rapidly and does not easily warp, cup, end check,

## Slide 5: PAULOWINA
splinter or split. Movement in service is rated as small.
Paulownia has one of the lowest thermal conductivity values of any wood; therefore the wood has very high insulation properties. Low thermal conductivity contributes to the low shrinkage in use.
Compared to most woods, Paulownia has a high resistance to fire and flames and a higher ignition/flash point. Paulownia is naturally decay resistant and any rot is generally superficial. The wood is also naturally resistant to insect attack.
Paulownia has no measurable pitch, resin or tannins so it is not subject to extractive bleeding.

## Slide 6: All types of usage
Working Properties
Paulownia is easy to work using hand or machine tools. It is easy to plane, sand, saw, rip, route, and carve, and even during quick processing there is no danger of splitting or chipping. It easily absorbs glue, paint and stains.

## Slide 7
Wood Utilization/Uses - Exterior/Interior Trim Boards - Exterior/Interior Pattern Stock - Paneling/Siding - Box Columns - Extension Jambs/Flat Jambs - Millwork | Summary of Benefits - Mostly Plantation Grown - Dimensionally Stable - Low Shrinkage Coefficient - Light Physical Weight - High Strength to Weight Ratio - High Insulation Properties - High Fire and Ignition Resistance - Low Thermal Conductivity - Contains No Measurable Tannins, Resin or Pitch - Easy to Nail, Screw or Staple - Light Color - Straight Grain - Easy to Work with All Tools - Easy to Handle - Easy to Glue, Stain and Paint - Naturally Rot, Decay and Insect Resistant - Glossy, Lustrous Finish

## Slide 8
Products Offered
offers a wide range of primed products made of Paulownia Sherwin-Williams Primer Optional. All Paulownia products are standard 16' Lengths. 18' & 20' & custom lengths available.

## Slide 9
Boards & Dimension
Kiln Dried S4S or S1S2E Square or Eased Edge FJ and or FJ/EG Exterior Waterproof Glue Exterior Oil Base Spray Primed 4 Sides & Both Ends 180 Grit Sanded 4 Sides After Priming One or Two Coat Primed Standard ALS Widths-Custom Thickness & Widths Available Fully Reversible

## Slide 10: Primed boards
Standard Product Line: | 
4/4 (11/16") - 1 x 2, 1 x 3, 1 x 4, 1 x 5, 1 x 6, 1 x 8, 1 x 10 & 1 x 12 4/4 (3/4") - 1 x 2, 1 x 3, 1 x 4, 1 x 5, 1 x 6, 1 x 8, 1 x 10 & 1 x 12 5/4 (1 1/8") -5/4 x 3, 5/4 x 4, 5/4 x 5, 5/4 x 6, 5/4 x 8, 5/4 x 10 & 5/4 x 12 8/4 (1 1/2") - 2 x 2, 2 x 4, 2 x 6, 2 x 8, 2 x 10 & 2 x 12 | 

## Slide 11: Pattern stock
Pattern Stock
Kiln Dried S4S - Square Edge S2S - tongue and groove FJ and or FJ/EG Exterior Waterproof Glue Exterior Oil Base Spray Primed 4 Sides & Both Ends 180 Grit Sanded 4 Sides After Priming One or Two Coat Primed Fully Reversible

## Slide 12: Stocking patterns
Standard Product Line: | 
1 x 4 & 1 x 6 T & G Beaded Ceiling - EB & CB/V2E 1 x 6 & 1 x 8 Plowed for Soffit Custom Patterns Available | 

## Slide 13: Bevel stock
Bevel Sidings | 
Kiln Dried Smooth Face/Re-Sawn Face Eased Edges & Tip FJ and or FJ/EG Exterior Waterproof Glue Exterior Oil Base Spray Primed 4 Sides & Both Ends 180 Grit Sanded 3 Sides After Priming One or Two Coat Primed Fully Reversible | 
Standard Product Line: | 
 | 1/2 x 4, 1/2 x 6 & 1/2 x 8 11/16x 6, 11/16x 8 & 11/16 x 10 3/4 x 8 & 3/4 x 10 5/8 x 6, 5/8 x 8 & 5/8 x 10 Custom Sidings Available

## Slide 14: Timbers
Timbers | 
Kiln Dried S4S Square or Eased Edge FJ and or FJ/EG Exterior Waterproof Glue Exterior Oil Base Spray Primed 4 Sides & Both Ends 180 Grit Sanded 4 Sides After Priming One or Two Coat Primed | 
Standard Product Line: | 
 | 4 x 4 Custom Sizes Available

## Slide 15: PAULOWNIA lightweight-stable decay&insect resistance

## Slide 16: Protect your best investment

## Slide 17: TRIP THOUGH THE PLANT

## Slide 18: Paulownia blanks

## Slide 19: Paulownia being planned

## Slide 20: Product being primed

## Slide 21: Hand sanding & patching defects

## Slide 22: Quality check on beaded pattern

## Slide 23: Drying racks

## Slide 24: Drying room

## Slide 25: Packaging paulownia

## Slide 26: Packaging product

## Slide 27: Packaging units

## Slide 28: Staging package units

## Slide 29: Loading trucks

## Slide 30: TRUCK GOING TO DOCK TO LOAD IN VANS

## Slide 31: ADDITIONAL INFORMATION SHEETS
MSDS SHEETS * ON GLUE IN PRODUCT * ON PAULOWNIA WOOD * ON PAINT/PRIMER WARRANTY ON PRODUCT * 10 YEAR WARRANTY * AGAIN FJ FAILURE * AGAIN ROT OR DECAY * INSECT RESISTANT ADDITIONAL INFORMATION *WWW.SANTIAMLUMBERSALES.COM