| Connector Part Information | • 12110088 • 24-Way F Micro-Pack 100 Series (GRY) |
| --- | --- |
| Pin | Wire Color | Circuit No. | Function |
| A1 | BRN/WHT | 419 | MIL Control |
| A2 | DK BLU | 507 | Wait to Start Indicator Control (Diesel Only) |
| A3 | BLK/WHT | 174 | Low Washer Fluid Indicator Supply Voltage (Except 4.3L w/o YE9) |
| A4 | DK GRN/WHT | 817 | Vehicle Speed Signal |
| A5 | WHT | 121 | Engine Speed Signal |
| A6 | GRY | 1036 | IPC Class 2 Serial Data |
| A7 | -- | -- | Not Used |
| A8 | DK BLU | 2115 | Right Turn Signal Lamps Supply Voltage |
| A9 | DK BLU | 2713 | Supplemental Brake Assist Signal (w/ SBA) |
| A10 | DK GRN/WHT | 1932 | Transmission Shift Select Switch (Park) Signal |
| A11 | RED | 2353 | Instrument Panel Lamps Dimming Supply Voltage |
| A12 | BLK | 1050 | Ground |
| B1 | LT BLU | 2114 | Left Turn Signal Lamps Supply Voltage |
| B2-B3 | -- | -- | Not Used |
| B4 | ORN | 1816 | DIC Mode Switch Signal |
| B5 | DK BLU | 894 | DIC Toggle Switch Signal |
| B6 | DK GRN/WHT | 1358 | DIC Switch Signal |
| B7 | YEL | 1327 | DIC Fuel Signal |
| B8 | -- | -- | Not Used |
| B9 | PNK | 639 | Ignition 1 Voltage (w/o 8S8) |
|  | PNK | 739 | Ignition 1 Voltage (w/ 8S8) |
| B10 | -- | -- | Not Used |
| B11 | ORN | 2840 | Battery Positive Voltage (w/o 8S8) |
|  | ORN | 4540 | Battery Positive Voltage (w/ 8S8) |
| B12 | BLK/WHT | 1851 | Ground |