## AUTO CAL II

233 Safety Road

Houma, LA  70363

Tel # 985-868-1477  Fax # 985-879-1617

e-mail - autocalflow@aol.com

www.autocalflow.com

### Operating Instructions

#### American System

SW 1      SW 2       SW 3      SW4           SW5       SW6

Switch 1 – Power on and power off.

Switch 2 – Sets computer in operation or calibration mode.

Switch 3 – (a)  Sets calibration code when switch 2 is in Cal position.

- Extends or retracts servo when switch 2 is in Cal position.

This feature is used during maintenance or emergency and

can not be used for spraying.

Switch 4 – Sets desired swath width.

Switch 5 – Sets sensitivity of system.

Switch 6 – Sets desired rate.

Date 11.01.2017			Page 1

##### Display

Height 2.5” – Width 4.5” – Depth 1.1” – Weight .3 lbs

- GPS – Gallons per acre desired.

- GPM – Gallons per minute being pumped through booms.

- REQ GPM – Gallons per minute required at your current speed.  Auto Cal II will automatically and continuously adjust flow to match REQ GPM when spray system is on.  Upwind, downwind, heavy or light aircraft, Auto Cal II will maintain your selected rate per acre.

- SENS – This setting controls the sensitivity of the actuator or other controllers.    It controls the minimum movement.  Settings to high will cause boom pressure fluctuations.

##### General Guidelines

  - 15 is the maximum setting for servo.  100 for hydraulic or electric.

  - Keep setting as low as possible.

  - A setting of 6-12 for servo or 40-50 for hydraulic or electric is an average place to start.

  - If GPM and required GPM are too slow matching up, bump up the SENS setting.  Keep in mind that this will never be instantaneous, the display has a small delay.

  - CAUTION – Excessive play in the bell cranks, rod ends and spray valve must be kept to a minimum for Auto Cal II to perform at its peak.

  - Suggested Sens – Servo 8, Hydraulic or Electric 50.

- APM – Acres per minute being covered at the current ground speed and selected swath width.  Optional – Servo position or gallons per acre, most units are shipped using this optional information.

- SWATH – Swath width selected in feet or meters.

- G/S – Current ground speed in miles per hour.

Date 11.01.2017								Page 2

###### Operating Auto Cal II

- Turn power on.

- Select “oper” for operation mode.

- Now the operator can select swath, width, sensitivity, or gallons per acre.  (These selections can be made anytime the system is receiving a GPS signal.)

- As the switches are operated, you can read your desired value on the remote display.

- The selectable values, GPA, sensitivity, swath and calibration codes are stored in memory.  The values will remain set even when Auto Cal II is shut down and powered up again.  New values are stored as the operator changes them.

- When warning light illuminates, the display will either read “GPS Signal Lost”, “GPS Bad 2”, or “Increase or Decrease Flow”.  When it displays “GPS Signal Lost” the unit is not receiving ground speed and stops working.  GPS Bad 2 indicates signal being received but not correct.  When the display reads “Increase Flow or Decrease Flow” this means the flow rate through the booms cannot be controlled with the Auto Cal due to adjustment problems.  To correct this problem, you should either adjust your fan, handle, or booms to adjust you boom pressure.  For some applications, the handle will probably need to be closed to fix the “Decrease Flow Warning”.

- When using a servo bypass regulating system, servo position is displayed above APM and should be used for help adjusting flow.  1450 is valve ½ open.  The fan should be adjusted for a no wind condition for the reading to be close to the 1450 number.  This will help the Auto Cal II to be on target entering the field.

- When turning on, the display will not advance to the spray screen if it is not receiving a GPS signal.  A switch can be selected and held before turning unit on and that switch will be active.  If a switch is not selected before turning unit on without a GPS, it cannot be selected without first turning unit off.

- When the first two switches are up (on and open) the third switch can be used to increase or decrease the servo position or voltages to the electric motor or the hydraulic controller.  This switch is used for presetting the dry gate opening to the desired position.

- The Auto Cal unit can be operated in the Cal mode without GPS to see gallons per minute that is being pumped while spraying.

Date 11.01.2017								Page 3

Calibration

Height 1-5/8th” – Width 3-11/16th” – Depth 5-3/4th” – Weight 1.0 lbs

SW 1      SW 2       SW 3      SW4           SW5       SW6

- Select Cal on switch 2.

- Switch 3 will increase or decrease cal code.

- Notice the display format changes.

- If you have SPD displayed in the cal mode, switch 6 will set the speed.  The speed is used as a minimum speed and can be used for a minimum flow out of booms.

- While pumping a known rate, gallons per minute, through the flow transducer, simply adjust cal code until the proper gallons per minute appears in the display.

- If you already have a crop hawk installed, simply adjust the cal code until gallons per minute matches GPM on your crop hawk.

- If you are sure of the area that you are spraying and you are not coming out on target, a small correction to the cal code will fix the error.

- Increasing the cal code will increase the amount of chemical being sprayed on the ground.  If you put a 10 acres load in and run out at 9 acres, you are applying 10% too much.  You would need to decrease your CAL code by 10%.  This would put you very close.  After this 1st adjustment, one or two numbers changed at a time should be done until the load fits the acres.

Date 11.01.2017								Page 4

Installation

- Locate desired position in cockpit for computer.  Preferred location is under instrument panel.  DO NOT mount on side where water can drip or where the pilot might step on switches.

- Install the display in full view of pilot.  The display gives warnings, and if something is wrong, the pilot should not have to look down to read the display.

- Install flow transducer adapter at a location that will allow interconnection with the flow transducer.  NOTE:  For crop hawk, the connectors are identical to crop hawk flow transducer and is simply a plug and play.  The Auto Cal, Crop Hawk, or Micron Air will operate independently of each other with the one flow transducer.

- Install a 5-amp circuit breaker in panel and label it “Auto Cal” Ref. 43.13.

- Connect power (RED) wire of system harness to 5-amp circuit breaker.  Only after other wiring is completed to prevent accidental damage.

- Connect ground (BLACK) wire of system harness to ground of aircraft at same location that the GPS is grounded to.

- All wiring, connection and routing to be I/A/W 43.13.

- For wiring diagrams and overall view of systems, see applicable pages.

- The average current on the Auto Cal II is less than 1 amp.  The maximum current is limited to 5 amps by the circuit breaker.

- The microswitch wire cannot share the same microswitch or relay contact that the GPS microswitch uses or damage will occur.

- The control board has fuses on it for protection.  Do not try to wire the system with power on or damage will occur.

- The 1/3 boom, ½ boom, and high low flow wires do not have to be used unless needed.  Open switch contacts are full boom and high flow.  Wires must have separate switch contacts.  No external power to contacts.

For any questions regarding installation, parts or operation, please call, email, fax or write the factory at 233 Safety Road – Houma, LA 70363 – (Tel) 985-868-1477 –

(Fax) 985-879-1617 – (email) autocalflow@aol.com. - (web) autocalflow.com

Date 11.01.2017								Page 5

###### Block Diagram

NOTES:

- Units are made as 14 Volt or 28 Volt only.

- A WET only or DRY only will not have a wet/dry switch.

- The Flow Adapter is for wet and it will vary depending upon type of Flow Transducer used.

- A Trimble, AgNav, Satlock, or Garmin GPS interface is not interchangeable.

- The Wet Servo and Dry Servo will both run on either cable, but the servos have different gearing and length.

Date 11.01.2017								Page 6

###### Installation of Flow Transducer Wiring

(If aircraft has Flow Meter installed)

###### Installation of Flow Transducer

(Typical on all models)

Install I/A/W aircraft manufacturer’s installation procedure, typical instructions listed below:

- Cut and remove a section of pipe between spray valve & spray boom.

- Install flow transducer using hoses and clamps.

- Route transducer wiring up to the flow adapter.

Date 11.01.2017								Page 7

By Pass Regulating System

Auto Cal Bypass Valve Setup

This system re-circulates anything not needed by the boom, back through the pump.

The servo position is shown on the Auto Cal Display above HPM (Hectors Per Minute) or APM (Acres Per Minute).

If it is reading Below 350, the valve should be open.

If it is reading Above 2100, the valve should be closed.

If it is reading Between 1400 to 1500, the valve should be half opened.

This will be the place the valve goes while the aircraft is on the ground and receiving GPS signal.

The fan gets set to produce a position indication between 1400 to 1500 when spraying with no wind or with a crosswind.  The pilot's handle should be all the way OPEN.

To run the servo, switch SW 1 to the "ON" position, switch SW 2 to the "OPER" position.  When holding SW 3 (CAL Switch) in the up position, it will extend the servo.  When holding SW 3 in the down position it will retract the servo.  You will hear the servo when doing this.  It is very important that the servo position goes to the extended and retracted positions and stops clicking while you are holding the switch.  If clicking is still heard, a cable adjustment will be necessary.

Date 11.01.2017								Page 8

GPS INSTALLATION

Note:  This page does not apply when using existing spray GPS system to operate the Auto Cal II system.

- Using bracket supplied, locate and drill holes in to of fuselage.

- Drill ¼” holes for GPS cable.

- Apply sealer under bracket before tightening screws.

- Apply sealer around cable after pulling through ¼” hole.

Note:  GPS MOLEX PLUG INSTALLATION – The GPS is shipped without the plug installed to allow cable to fit through the ¼” hole in the aircraft.  The Molex plug is temporarily tied to the cable.  Remove the Molex plug, pull cable through hole drilled in aircraft, install pins per interconnect drawing.

Date 11.01.2017								Page 9

Date 11.01.2017															Page 10

Date 11.01.2017															Page 11

Ag Air Hydraulic Interconnect

Date 11.01.2017							Page 12

Date 11.01.2017							Page 13

Electric Motor Controller

B-, and M- have to be same size as wire used to run motor. Manual speed control can be set from off to full speed.

Switch allows for automatic or manual pump speed control by using the 5 K ohm pot for manual.

B+ jumper (20 gauge) to Red terminal on J1. B+ enables motor controller, a switch could be used on this wire that would make the controller act as an electronic solenoid.

M- gets ground wire from motor. No ground at motor, M- controls ground from motor.

Date 11.01.2017							Page 14

Date 11.01.2017													Page 15

Data Logger

Date 11.01.2017						Page 16

AUTO CAL - ACTUATOR FOR DRY

Cut Orange/White wire.  Add potentiometer as shown in the diagram above.  Mount the potentiometer where pilot can adjust it during flight.

To Operate:

Before starting:  Set pot at 1/2 position (centered).  Set actuator stop for 100 lbs or 100 kilos

In flight:  The pot can be used to increase or decrease the output without using the switches.  The switches can only be used on the ground.

On the ground:  Look at the handle stop on the actuator.  Set the pot back to the center, using the switches to reset the actuator to where it was before centering the potentiometer.  The system always uses 100 Kilos or 100 lbs as the default rate.  If the Cal Code is correct, and you go 75 on the rate, the handle will pull back to the 75 lb or 75 kilo position.  When you go back to 100, the stop will go to the 100 position.  To set the cal code, you must be using the same swath for both rates.  On later systems, if a 1/2 Boom Switch is installed, it can be used to go from 100 to 50 on the rate, for help in setting Gate Cal Code

Note:  When you change swath width, the 100 position will be different.  Look at the records for your airplane, for the new 100 position for the new swath width.  When the unit boots up, the speed shown is the average spray speed.  This can be set in the cal mode using the GPA or LPM switch.  Most speeds are set in MPH.  The Auto Cal Simulator only outputs knots or kilos.

Date 11.01.2017													Page 17

##### AUTO CAL CALIBRATION

AMERICAN

#### CAL CODES			FLOW RATES			JUMPER POSITION

TM0100 – Low Flow Position	Minimum – 5 GPM			Left Side

About – 155				Maximum – 50 GPM

TM0150 – High Flow Position	Minimum – 15 GPM			Left Side

About – 270				Maximum – 180 GPM

AC0200 – High Flow Position	Minimum – 40 GPM			Right Side

About – 137				Maximum – 400 GPM

AC0300 – High Flow Position	Minimum – 60 GPM			Right Side

About – 150				Maximum – 600 GPM

Crophawk 2” Flow meter jumper on the right side		Micronair Flow Meters that are the same size 		Basket #1 High Rate Flow / Cal Code = 260			as the Turbine Flow Meters would be the

Basket #2 Low Rate Flow / Cal Code = 210			same as the Turbines

Diagram represents Crophawk 2” – showing jumper in right position

(Spare pin on left side)

Move jumper to the left side (spare pin on right side) for TM0150 and smaller Flow Meters

If your display has FM on the screen when in CAL MODE, please see next page.

Date 11.01.2017								Page 18

FOR USE IF AUTO CAL DISPLAYS FM

FM IS FOR FLOW METER SELECTION - TO CHANGE THE FM, WHILE IN CAL, USE THE SWATH SWITCH - THERE IS A DELAY

AMERICAN CAL		HI/LOW FLOW 		CAL CODE		       GPM

SWITCH

FM 1	TM0038	           	          LO			       155		.30 TO 3.0 GPM

FM 2	TM0050	                      LO			       177		.75 TO 7.5  GPM

FM 3	TM0075	                      LO			       159		2.0 TO 15  GPM

FM 4	TM0078	                      LO			       186		3.0 TO 30  GPM

FM 5	TM0100 	                      HI			       246		5.0 TO 50  GPM

FM 6	TM0150	                      HI			       260		15  TO 180 GPM

FM 7	TM0200	                      HI			       140		40  TO 400 GPM

FM 8	TM0300	                      HI			       107		60  TO 600 GPM

FM 9	CROPHAWK	                      HI			       225 (MOVE JUMPER ON CONTROL 											     	    BOARD TO RIGHT SIDE)

FM 9	TM0100	                      LO			       155 (MOVE JUMPER ON CONTROL 											     	    BOARD TO LEFT SIDE)

FM 9	TM0100	                      HI			       500 (MOVE JUMPER ON CONTROL 											       	    BOARD TO LEFT SIDE)

FM 9	TM0150	                      HI			       260 (MOVE JUMPER ON CONTROL 	  										     	    BOARD TO LEFT SIDE)

WHEN USING FM 9 SETTING, THE CALIBRATION SETTINGS WOULD BE THE SAME AS 			FIRST PAGE AND YOUR CAL CODES WOULD BE THE SAME AS THEY WERE BEFORE THE 			CHANGE.

Date 11.01.2017								Page 19

FLOW METER SPECIFICATIONS

| PART # | FLOW AREA | CONNECTION TYPE | MIN / MAX LPM | MIN / MAX GPM |
| --- | --- | --- | --- | --- |
| TM0038 | .38 INCH | 0.5” MALE NPT 1.0” MALE NPT | 1.14 / 11.36 | .30 / 3.0 |
| TM0075 | .75 INCH | 0.5” MALE NPT 1.0” MALE NPT | 7.57 / 56.78 | 2.0 / 15 |
| TM0100 | 1.0 INCH | 1.0” MALE NPT | 19 / 190 | 5.0 / 50 |
| TM0150 | 1.5 INCH | 1.5” MALE NPT | 57 / 680 | 15 / 180 |
| TM0200 (TRUCK / TANK ONLY) | 2.0 INCH | 2.0” FEMALE NPT | 151 / 1500 | 40 / 400 |
| TM0300 (TRUCK / TANK ONLY) | 3.0 INCH | 3.0” VICTAULIC CONNECTOR | 227 / 2270 | 60 / 600 |
| AC0200 | 2.0 INCH | 2.0” W/CLAMPS, GASKETS, AND FERRULES TO BE WELDED TO PIPE | 151 / 1500 | 40 / 400 |
| AC0300 | 3.0 INCH | 3.0” W/CLAMPS, GASKETS, AND FERRULES TO BE WELDED TO PIPE | 227 / 2270 | 60 / 600 |

ADDITIONAL CABLE REQUIRED FOR FLOW METERS:

PT# AC10354-01

Date 11.01.2017								Page 20

# Text boxes

B+

Signal

5 Volts

Display

Warning

Ground

5 Amp.

C.B. 1

Ground

GPS Data Out

Data Input

GPS

14 or 28 Volts

Back Lighting

Controller

5 Volts

Flow

Adapter

Flow

Transducer

Signal

Ground

Ground

Servo Motor,            Hydraulic, or  Electric

Wet

Dry

Servo Position

Servo Motor, Hydraulic, or Electric

Servo Position

GPS Receiver

Optional GPS Receiver locations

GPS cable

Nylon

Tie-wrap

To Auto Cal Computer

Date 11.01.2017							Page 13A

25 amp BKR